## Slide 1: Vive Trackers for Unity3D

## Slide 2
Import the SteamVR plugin for Unity in your project:
https://assetstore.unity.com/packages/tools/integration/steamvr-plugin-32647
If applicable (depends on SteamVR plugin version), uncheck :
Preferences -> SteamVR -> Automatically Enable VR
Check : Project Settings -> Player -> XR Settings > Virtual Reality Supported
  Add VR SDK None
  Add VR SDK OpenVR
*ViveTrackersManager script automatically initializes OpenVR,
so we need to set the primary VR SDK to None
to prevent Unity3D to initialize OpenVR.
NB: The SteamVR application should always run in the background while the Unity3D application (either the UnityEditor or an executable) is running. If not, you should expect Vive Trackers connections issues !!!
Unity3D Configuration

## Slide 3
1. Vive Trackers calibration in Unity3D
In Unity3D, ViveTracker objects can be calibrated. The origin reference frame is used as the default transformation for their calibration.
*during runtime,
the origin reference frame
can also be used to apply an offset
(3D Position & Rotation) to all the trackers.
2. SteamVR Room calibration
If you need to get a perfect match between your virtual world and your real world (e.g. going towards a direction in the real world applies the same direction in the virtual world), you should make the SteamVR reference frame aligned with the desired forward axis in your real space.
*each time a SteamVR calibration is done, the application using the Vive Trackers must be restarted (e.g: UnityEditor).
SteamVR reference frame in the real space
Understanding SteamVR calibration and Vive Trackers calibration
SteamVR reference frame

## Slide 4: SteamVR configuration

## Slide 5
Modify these SteamVR configuration files:
SteamFolder/steamapps/common/SteamVR/drivers/null/resources/settings/default.vrsettings
  > set enable to true
SteamFolder/steamapps/common/SteamVR/resources/settings/default.vrsettings
> set requireHmd to false
> set forcedDriver to null
> set activateMultipleDrivers to true
More informations:
http://help.triadsemi.com/en/articles/836917-steamvr-tracking-without-an-hmd
Running SteamVR with Vive Trackers only (no HMD)

## Slide 6
Set SteamVR properties in Steam
NB : Be careful when Steam performs a SteamVR update :
default.vrsettings files could be overridden with new ones !!!
Force SteamVR to update itself only when Steam is launched
Recent versions of SteamVR have good support for Vive Trackers. So, you can avoid beta versions.

## Slide 7: Optimize Vive Trackers connection reliability

## Slide 8
Configure Windows Power Options

## Slide 9
Set SteamVR settings
SteamVR will update itself only if Steam is executed !